## Slide 1: On the Use of MDPs in Cognitive Radar: An Application to Target Tracking
May 3, 2018
Ersin S. Selvi
Mark Kozy
R. Michael Buehrer

## Slide 2: Introduction
Radio spectrum is a precious resource which is getting more and more congested
Spectrum sharing between disparate services (e.g., communications and radar) is becoming a reality
Cognitive radio and cognitive radar have emerged as potential solutions to the coexistence problem
The concept of cognitive radar allows radars to learn (or be trained) to modify its parameters to maximized a pre-determined performance metric

## Slide 3: Problem Statement
A tracking radar and one or more communication systems attempt to co-exist in the same spectrum consisting of N sub-bands
The radar attempts to maximize both bandwidth and SINR which are conflicting requirements due to possible interference
  Wider bandwidth desired for finer range resolution
  Higher SINR desired for better tracking performance (less variance on range/velocity estimates)
  Large degradations in SINR may lead to a loss of target
Can we incorporate machine learning into a radar system to allow it to optimize its performance while sharing the spectrum with a communication system?

## Slide 4: Radar Environment
Set of position

## Slide 5: Radar Environment (cont.)

## Slide 6: Radar Environment
Targets travel through the environment and are mapped to specific target states
Trajectories are varied and random
Initially interference is independent of target position (temporal correlation only)

## Slide 7: Assumptions and Limitations
State space is kept reasonably small for runtime considerations (~5000 total states)
Assumes that spectrum usage of comm system has structure
Simple point target moving roughly orthogonal to boresight (exact trajectory is random)
All radar signal processing is abstracted
  Clutter, multipath and atmospheric effects are negligible (SINR based on target range and interference power)
Only contiguous bands considered for radar transmission
Spectrum observations and target measurements are ideal

## Slide 8: Offline Training
Training length 1000-100000 depending on the scenario
Training provides estimates of transition and reward matrices
Standard policy iteration technique used for solving MDP to provide policy

## Slide 9: Training Trajectories
Trajectory of the target is chosen randomly during training.
Target trajectories are generally orthogonal to boresight

## Slide 10: Trajectory for Results in this Presentation
We tested with other trajectories but only show results for this one.
The results for other trajectories are similar.

## Slide 11: Interference Cases Studied
Constant interferer
  Interference is always present
Intermittent interferer
  Interference may or may not be there on next time instant
Frequency Hopper
  Triangle sweep
  Sawtooth
  Pseudo-random
Direction-dependent interference
  Constant
  Intermittent

## Slide 12: Reward Structure
SINR = post processing
Reward structure can be altered to obtain a specified behavior
Incremental improvement in SNR not as valuable as bandwidth in this structure
SINR increases above 20dB not valuable
Negative SINR heavily penalized

## Slide 13: Assumed Timing
Simulation is time-slotted.
It is assumed that observations at time slot n lead to actions at time n+1.
It is also assumed that the state transitions are possible (i.e., the interference can change) at time n+ 1.
Based on the observations at time slot n, the radar anticipates the next state and acts accordingly
t
f
Observations
f
Interference
f
Actions
Slot n
f
f
f
Slot n+1
f
f
f
Slot n+2

## Slide 14: Constant Interferer
  The radar learns
    Specific structure of interference
    Avoid interference when target is farther away
    Occupy max bandwidth (i.e., ignore interference) when target is closer
  When the target is closer, radar trades excess SINR to increase bandwidth
  Specific behavior dictated by reward structure
Interferer
Radar

## Slide 15: Intermittent Interference (10%)
Learns that interference is not common
Best long-term behavior is to occupy entire band and suffer occasional SINR loss

## Slide 16: Intermittent Interference (90%)
Learns that interference is common
Treats interference as if it were always present
Avoids the interference band until range is below some threshold

## Slide 17: Sawtooth Interference Pattern
Interference Behavior
Observation
Next state
Action
Precedes

## Slide 18: Triangle Sweep
Interference behavior

## Slide 19: Improvement with Increased Memory
Drops in SINR due to lack of ability to predict hopping behavior in some states
Issue can be addressed by adding memory

## Slide 20: Triangle Sweep with Increased Memory
Interference behavior can now be predicted
Allows better planning
Avoids interference completely

## Slide 21: Pseudo-random Hopping (Length 5)
Radar learns the pattern and anticipates the correct waveform to use based on observation.

## Slide 22: Pseudo-random Hopping (Length 10)
The sequence length is greater than the memory (it cannot predict the next band based on the current band)
Radar choose the bands that provide best average reward based on two possible next states
Trades SINR for bandwidth when that is optimal on average

## Slide 23: Pseudo-random Hopping (Length 10)
Adding memory provides benefits
Can now anticipate the interference behavior and act accordingly

## Slide 24: Pseudo-random Hopping (Length >> 5)
Cannot learn pattern because next state does not depend only on previous state (Markovian property violated)
Best option is to use all of the bands all of the time
If bandwidth were valued less, would reduce bandwidth to reduce probability of interference

## Slide 25: Direction-Dependent Interference
Interference occurs only when target is in certain range (position) cells
Radar attempts to learn when interference will occur based on position state

## Slide 26: Direction-dependent Interference
Interference always present at certain target locations
Radar learns
  The sequence of position/velocity states
  The association of interference with position

## Slide 27: Direction-dependent Interference
Interference is intermittent but only at certain target locations
Radar learns to ignore the interference because it is rare

## Slide 28: Rewards Structure Analysis
The rewards structure is what defines the behavior of the radar
We experimented with various reward structures to determine the roles each aspect of the rewards played
Goal was to understand the specific role of each aspect and allow us to produce specific desired behavior
The rewards structure is comprised of a
  negative SINR penalty
  contiguous bands reward,
  SINR rewards layout
  SINR cap

## Slide 29: Rewards Structure Cont.
The negative SINR penalties mainly determines when the radar chooses to switch to all bands and take the SINR hit that comes from operating in a band with interference
With full bandwidth but negative SINR, overall reward is 15
With partial bandwidth and positive SINR, overall reward is 12
With full bandwidth but negative SINR, overall reward is 5
With partial bandwidth and positive SINR, overall reward is 12

## Slide 30: Rewards Structure Cont.
The other three aspects of the rewards structure all contribute to the timing of when the radar deems it acceptable to switch to full bands
Mainly what these aspects control is what we consider to be most desirable, if we want to maximize SINR or if we want to maximize the number of bands we want to operate in

## Slide 31: Multiple Interferers
Two intermittent interferers with a probability of 0.9 of the band being occupied
The results are similar to a single interferer case
Training runs took longer and required more runs to produce accurate results

## Slide 32: Temporal Interference Statistics
[1] An example of a real interferer that shows the short time scale
znd the long time scale
The majority of research concludes
  Interference generally follows Poisson distribution
  I.e., busy and idle periods within bands follow an exponential distribution
  This is true for the long time scale
Some research shows that there are also short time scale busy and idle periods during these long time scale busy periods
These short time scale busy and idle periods follow a Generalized Pareto distribution

## Slide 33: Results with Temporal Correlation
No added memory
Only learns probability of interference, but not temporal correlation
Without additional memory, performance is sub-optimal
Radar generally behaves like DSA Node
  It merely reacts to changes in interference
Currently working to add memory

## Slide 34: Conclusions & Caveats
In this work we have demonstrated that MDP-based cognitive radar can effectively learn
  MDP-based approach essentially learns what is optimal against the appropriate type of interference
  Learns: (a) relative frequency of interference, (b) interference state transitions (when they exist), (c) location dependence, (d) impact on rewards
Reward structure can be easily tailored for desired behavior
Sufficient training is needed
  Requires sufficient exploration of the state space
  Assumption is that this can be done offline using synthetic data
  We believe that with proper initialization, online training is possible
Impact of non-ideal radar signal processing and spectrum sensing were not fully explored

## Slide 35: Going Forward
In order to model more sophisticated temporal behavior we will need to modify the model
  Example: Examine the previous 5 time steps to help determine the future action of the interference so that the radar can respond accordingly
  This will require either more states or changing to a different RL approach (Q-learning or Deep RL)
Other challenges that will be investigated this summer:
  Speeding up learning
  Online learning/adaptation
  Performance guarantees during learning
  Performance against specific interference types
  Impact of imperfect observations

## Slide 36: Questions?